Introduction to Arduino
Presented by House 4 Hack
What will you build next?

---
Housekeeping
- We will be busy from 10:00 to 14:00
- It will be practical and interactive
- Feel free to move around, go for a smoke break, etc
- We will have a formal break half way through
- Experiment!
- Ask!
- Enjoy!

---
Interactive computing
digital inputs and outputs and PWM
USB
9v
input
analogue
power

---
Shields for the Arduino
Shield Examples
Voice recognition
Joystick
Bluetooth
Wifi
RF
Touch TFT LCD
Relay
Gameduino

---
Arduino Kit
Check that you have everything in your goodie bag
Arduino UNO
Breadboard
USB A-male to B-male
Components
Resistors: 100Ω,220Ω, 1kΩ, 10kΩ, 100kΩ
LED: red, yellow, green, RGB
Tactile Switch
Rotary pot 10kΩ
LDR – light dependant resistor
Relay, transistor and diode
Servo
1000 uF Capacitor

---
Blink Example
Getting Started
Make sure IDE is installed
Make sure USB drivers are installed
http://arduino.cc/en/Guide/HomePage
Connect Arduino to USB
Run the Arduino software
First Project (Code is caseSensitive)
Go to File > Examples > 01.Basics >Blink
Compile and load to board (Errors?)
Pin 13 on Arduino has a LED connected already

---
Breadboard

---
Resistor Chart
220Ω
Current limiting for LED
10kΩ
Pull down resistor for buttons

---
LED – Light Emitting Diode
Positive
Long pin
Rounded side
Negative
Short pin
Flat side
Remember to use your 220Ω resistor to
reduce the current through the LED

---
Blink Example on Breadboard

---
Fade Example
Fading an LED from ON to OFF
Open the "Fade" example
Compile and load to board
Notice the ~ on certain IO
Things to note
Pulse Width Modulation
Vary with 255 values
Use analogWrite
PWM(0) ~ 0V
PWM(127) ~ 2.5V
PWM(255) ~ 5V

---
DigitalReadSerial Example
Using a push button with Serial Monitor
10k resistor (Pull Down to prevent floating)
Push Button
Upload to board and open serial monitor
Serial.begin(9600);
Press the button

---
DigitalReadSerial Example
...continued
When you draw the "breadboard" layout in Fritzing it automatically creates the circuit diagram, you can even do basic PCB layouts from the schematic

---
Press the Button to change RGB Color
void loop(){
  sensorValue = digitalRead(sensorPin);
  if(sensorValue != lastSensorValue) {
     if(sensorValue) {
        mode ++;
        if(mode==3) mode=0;
     }
  }
   analogWrite(redPin,255);
   analogWrite(bluePin,255);
   analogWrite(greenPin,255);
  if(mode == 0){
     analogWrite(redPin,0);
  } else if (mode==1){
     analogWrite(greenPin,0);
  } else {
     analogWrite(bluePin,0);
  }
}

---
RGB LED
Red, Green and Blue in one LED.
void setup() {
    pinMode(9, OUTPUT);
    pinMode(10, OUTPUT);
    pinMode(11, OUTPUT);
}
void loop() {
    analogWrite(9, random(255));
    analogWrite(10, random(255));
    analogWrite(11, random(255));
    delay(500);
}
+5V
220 ohm
+
-
9 10 11

---
Structure of a sketch
// Global variables go here
int variable1;
long variable2 = 100;
double variable3;
void setup() {
    // This only runs once
    pinMode(9, OUTPUT); // for output
}
void loop() {
    // This is the super-loop, keeps executing
    int localvariable = 1;
}

---
AnalogReadSerial Example
Connect on breadboard
Middle pin goes to A0
Open Serial Monitor
Serial.begin(9600);

---
Turn Pot to Change RGB Color
void loop(){
sensorValue = analogRead(sensorPin);
analogWrite(redPin,255);
analogWrite(bluePin,255);
analogWrite(greenPin,255);
if(sensorValue < 330){
    analogWrite(redPin,0);
  } else if (sensorValue < 660){
    analogWrite(greenPin,0);
  } else {
    analogWrite(bluePin,0);
  }
}

---
LDR – Light Dependant Resistor
Add your own code:
As the light level changes - changes the RGB LED values?

---
Servo – Knob Example
Servo Library
"Knob" example
Servo driven by PWM
The servo you have can only rotate 180 degrees
This one heavy on the juice (500mA)
Use the big cap to sort out your power supply!
Note:
Servo colors may vary, e.g. Red, White, Black – consult the datasheet for pinouts

---
Relay
External circuits:
Irrigation System
Fan
Arduino maximum current out per pin 40 – 50 mA

---
Acknowledgements
Tutorials from Arduino.cc, and various authors on countless forums. To these authors our thanks and acknowledgement

---
Contact info
Email
Schalk:	   	schalk.heunis@gmail.com
Guy:	guy.vandenberg@microsmart.co.za
Find us
h4h website:	http://www.house4hack.co.za/
h4h Google group:	https://groups.google.com/forum/#!forum/house4hack

---
Upcoming courses
- Advanced Arduino
  - AT Tiny
  - SD Card
  - SPI, I²C
- Internet of Things
  - Build an online electricity meter!